Title
Developing a rigorous bottom-up modular static failure modeling methodology
Robin Clark # Energy Technology Control Ltd

---
Long-term Goal
Background: Certification of Safety Critical products
- Environmental Stress
- Endurance
- Electromagnetic Compatibility
- Device specific testing
- Static (theoretical) Testing using FMEA, FMEDA etc

---
Customer Wishes
Static Testing
- Failure scenario based: often incomplete only areas perceived as critical examined
- FMEA type analysis links component failure modes to top level errors, with little analysis of side effects in other components
- State explosion problem. Looking at the effect of all component failure modes on all other components in a system is impractical due to state explosion.
- Difficult to access multiple simultaneous failures.

---
Fulfilling Customer Needs
A better Static testing methodology would...
- Address the state explosion problem
- Consider all possible component failure modes, and a reasoning path to all top level events
- Allow integration of mechanical, electrical and software models.
- Have a formal bases and traceability
- Be able to model simultaneous failures

---
Cost Analysis
A proposed methodology: Failure Mode Modular De-Composition(FMMD)
- Should be bottom-up to ensure including all component failure modes
- Should model in terms of failure modes only, so that mechanical, electrical and software components can be modeled
- To address state explosion it should group components into small functional groups, which when analyzed are treated as components, which can form higher level functional groups.
- As it is modular specific multiple failures can be modeled.
- Because his process form a hierarchy, the reasoning is traceable.

---
Strengths and Advantages
FMMD Outline
- Create functional groups of components
- Analyze the effects of all failure modes within the functional group, and determine the symptoms of failure for the functional group.
- Create a derived component to represent the functional group, where its failure modes are its symptoms
- Use derived components to form higher level functional groups, and higher level derived components
- A hierarchy is built which will converge to a set of top level failure modes, or “system” failure modes.

---
Next Steps of Action
An Example: A non inverting Amplifier

---
Functional Groups
- We can begin to analyse this by looking for functional groups.
- The resistors would together to perform a fairly common function in electronics, that of the potential divider.
- We can now take the failure modes for the resistors (OPEN and SHORT EN298) and see what effect each of these failures will have on the functional group.

---
Resistor Failure modes as graph

---
Failure mode analysis of potential divider
Failure Scenario		Pot Div / Effect		Symptom
FS1: R1 SHORT		LOW		PDLow
FS2: R1 OPEN		HIGH		PDHigh
FS3: R2 SHORT		HIGH		PDHigh
FS4:		LOW		PDLow

---
Potential Divider as a `derived component'.

---
Opamp failure modes

---
Functional Group formed by derived component PD and OPAMP